README file
The H265 2-dimensional Inverse Integer transform has 4 steps.
1) For each row calculate the 1-dimensional transform.
Mathematically, this is a matrix multiply operation.
2) Scale each number in the resulting matrix by 128 and round.
3) Next, for each column of the resulting matrix, calculate the
same 1-dimensional transform.
4) Scale each number in the resulting matrix by 128 and round.
----------------------------------------------
The VHDL code here is for the 1-dimensional Discrete Cosine Transform of 4-points,
i.e. steps 1 and 2 shown above.
The link to other 2-dimensional Transform Units form Transformvid Corp. is here:
www.transformvid.com

[You may need to cut link and paste in browser.]
The input data matrix, A, is defined as [f0 f1 f2 f3]. Size is 1 x 4.

The transform matrix, B, is defined as a fixed 4 x 4 matrix. Size is 4 x 4.
64 64 64 64
83 36 -36 -83
64 -64 -64 64
36 -83 83 -36

The VHDL code performs A X B matrix operation, which results in size 1 x 4.
Each resulting number has been divided by 128 and rounded.
----------------------
Two files are enclosed.
1) VHDL code of 1-dimensional transform.
2) Testbench file with some examples.
Create a project in Vivado and add both sources, then "RUN SIMULATION".
The testbench (tb) will supply the input data and check output results. If there is an error, the tb
will state "ERROR", the matrix number that is in error, and the simulation time.
--------------------------
Please note:
The input order to the transfrom block is:	f3	f1	f0	f2
The output order from the transform block is:	m0	m1	m2	m3
-----------------
The core is available in synthesizable VHDL and FPGA netlist forms. It provides everything required for successful implementation, including a sophisticated self-checking testbench, test vectors, and expected results, and comprehensive user documentation.
----------------------
Copyright © 2021 Transformvid Corp. All rights reserved.

email:	support@transformvid.com
office: 949-873-5088